## Slide 1
CT super-resolution using
deep Convolutional Neural Network

## Slide 2: Abstract
Data : training – 52set, test – 13set
Validation : 5-fold cross-validation
Experiment for resolution, contrast, noise properties
Improvement :
  deblurring of boundaries of bone structures and air cavities
  10% higher peak SNR, lower normalized root mean square than input
  Output noise level : lower than ground truth, equivalent to iterative reconstruction result

## Slide 3: Introduction
CT : immense amount of acquired data -> longer scan range & slower operating speed
Using small angle views with a thicker slice thickness -> recon
Reconstructed slice thickness ↓
  Z-axis resolution ↑
  Noise ↑
  Dose ↑
Without dose ↑ , noise ↑ , enhance CT img resolution (similar to using thin slice)
CNN : good at super-resolution, de-noising
CNN base super-resolution approach -> some drawbacks in biomedical image processing
  Network run for each patch -> redundancy -> slow computation
  Trade off between localization accuracy and use of context
    Large patch : use large context but max pooling ↑ -> localization accuracy ↓
    Small patch : use little context -> localization accuracy ↑

## Slide 4: Introduction
U-Net : provide end to end mapping architecture
  Contracting path : capture the context
  Expanding path : precise localization with large receptive field
Main purpose : CNN is also useful for CT image super-resolution
end-to-end mapping between low and high resolution imgs using modified U-Net
Performance : resolution↑, contrast↑ & noise↓

## Slide 5: Materials and methods
Data : 65 clinical PET/CT studies for brain with suspected Parkinson’s disease
  CT : 512 X 512 X (60 - 80)
  Training dataset : 5 slices of a 3mm thickness -> averaged into 1 slice of 15mm thickness / 52 patients
  Ground truth : middle slice of five slices (high resolution) / 13 patients
5 – fold cross-validation
Input : thick slice(low resolution) /Output : thin slice(high resolution)
  2D slice
  Total number of slice for training : 7670

## Slide 6: Materials and methods
Network architecture
  end to end mapping between thinner and thicker slice images
  Architecture : contracting path & expanding path (symmetrical, each path : 5 sequential layer)
Contracting path : capture the context
  Typical CNN architecture
  Each layer : two [conv(3X3) → BN → ReLU] => max pooling(2X2, s = 2)
  mini-batch size : size of six images
Expanding path : enable precise localization
  Each layer : up-sampling(s = 2) => two[conv(3X3) → BN → ReLU]
  Last layer : 1X1 conv for scaling
  Skip connection between conv layer and deconv layer
Propagate context information to higher resolution layer

## Slide 7: Materials and methods
512X512X1
512X512X32
Conv
3X3
Same
s=1
f=32
512X512X32
Conv
3X3
Same
s=1
f=32
256X256X32
max
2X2
valid
s=2
256X256X64
Conv
3X3
Same
s=1
f=64
Conv
3X3
Same
s=1
f=64
max
2X2
valid
s=2
128X128X64
128X128X128
Conv
3X3
Same
s=1
f=128
128X128X128
Conv
3X3
Same
s=1
f=128
64X64X128
max
2X2
valid
s=2
Layer 1
Layer 2
Layer 3
Conv
3X3
Same
s=1
f=256
64X64X256
Conv
3X3
Same
s=1
f=256
64X64X256
max
2X2
valid
s=2
32X32X256
Layer 4
32X32X512
Conv
3X3
Same
s=1
f=512
32X32X512
Conv
3X3
Same
s=1
f=512
Layer 5
Each conv
: conv -> BN -> ReLU
256X256X64

## Slide 8: Materials and methods
32X32X512
skip connection from layer 4
upconv
2X2
s=2
128X128X256
Conv
3X3
Same
s=1
f=256
L4
64X64X256
64X64X256
64X64X256
Conv
3X3
Same
s=1
f=256
64X64X256
upconv
2X2
s=2
L3
128X128X128
128X128X128
Conv
3X3
Same
s=1
f=128
Conv
3X3
Same
s=1
f=128
skip connection from layer 3
128X128X128
128X128X128
upconv
2X2
s=2
L2
256X256X64
256X256X64
256X256X128
Conv
3X3
Same
s=1
f=64
256X256X64
256X256X64
Conv
3X3
Same
s=1
f=64
skip connection from layer 2
upconv
2X2
s=2
L1
skip connection from layer 1
Conv
3X3
Same
s=1
f=32
512X512X64
512X512X32
512X512X32
64X64X512
512X512X32
Conv
3X3
Same
s=1
f=32
512X512X32
512X512X1
Conv
1X1
Same
s=1
f=32
# Channel ↓
Each conv
: conv -> BN -> ReLU
Layer 6
Layer 7
Layer 8
Layer 9

## Slide 9: Data training and loss function
Weight : truncated normal distribution
Loss function : L2 Loss
  F(Yi) : reconstructed image from low-resolution image Yi
  Xi : high resolution label image
Activation function : ReLU
Optimizer : Adam
Epoch : 18
n : #imgs in mini-batch
m : #layer
t : iteration number
: update parameter(weight/bias)
τ : learning rate
, : moment vector (initialized to zero)
: 0.9 : 0.999 :

## Slide 10: Image analysis
Evaluation : 13 patients data (5 – fold cross validation among 65 patient data sets)
Image quality metrics
  Peak signal-to-noise ratio :
  Normalized root mean square error :
Comparison : 3D Richardson-Lucy deblurring algorithm
  Kernel size of the point spread function : 3X3X3(pixel)
  sigma = 1
  → larger kernel size & larger sigma : too noisy
X(i,j) : high resolution image
Y(i,j) : output image
, : max, min intensity of image
Highest PSNR, lowest NRMSE
(kernel size from 0.5 to 3.0 in step of 0.5)

## Slide 11: Image analysis
Compare PSNR, NRMSE of original input / RL deblurred input / network output
  ROI based SD compare to assess the noise characteristics of soft tissue
Additional verification for clinical practice : recover 1mm slice from 5mm slice
  Data : training - 56 patients(9302 slices) / test – 14 patients(2338 slices)
  CT : 512 X 512 X (180-200)
  Verification : ROI based SD comparison & 5 – fold cross-validation

## Slide 12: Results
Recovery from 3mm slice from 15mm slices
  1) image
  Remarkable improvement : Deblurring of boundaries of bone structures and air cavities
  Computation time : 30ms per slice
Input(15mm)
RL deblurring
CNN output
Ground truth

## Slide 13: Results
2) Quantitative analysis of PSNR, NRMSE
  40% higer PSNR, lower NRMSE than input(thicker slice)
3) ROI based standard deviation
  RL deblurring increase noise level

## Slide 14: Results
Recovery from 1mm slice from 5mm slices
  Image 3) ROI based standard deviation
  PSNR & NRMSE
Input(15mm)
RL deblurring
CNN output
Ground truth

## Slide 15: Discussion
Show the potential of deep-learning based super-resolution of x-ray CT images
  Thick CT image : higher SNR (higher number of x-ray quanta per voxel)
  → CNN generated output : indistinguishable from ground truth
Not analyze the impact of super-resolution on lesion detectability
  Useful for previewing CT image reconstruction
Thick CT slice : low soft-tissue contrast, high noise level
  Reduce artifacts(insufficient angular sampling)
Limitation
  The proposed method use 2D CNN
  CNN super-resolution : expect to reproduce small structure

## Slide 16: Discussion
Spatial resolution of CT image : determined by the size of detector elements
  Development of new detector : time intensive, high cost
  Smaller detector element : increase noise
  sharpening (HPF) / deblurring (Laplacian filter / Richardson-Lucy algorithm) → noise↑, not as effective as proposed method
Focus on image resolution and contrast recovery in the degraded images
→ proposed method : kind of deconvolution operation for axial spatial resolution recovery
CNN based super resolution technique : improve medical image quality & reduce scan time
Noise reduction in CT : important for reducing radiation dose & improving diagnostic power
→ proposed method : effective in noise reduction
SAFIRE
Proposed method
Ground truth